Introduction to Engineering Design Unit 2 Practice Test		Name:_________________

  - Construction Line	Very light lines to guide drawing other lines and shapes

  - Object Lines		Thick and dark, define the object

  - Hidden Line		Show interior detail not visible from outside the part. Dashed line

  - Center Line	Define the center of arcs, circles or symmetrical parts.  Half as thick as an object line, dashed.

  - Section Line	Define where material is cut away

  - Short Break Line	Freehand drawn line.  Shows where part is broken to reveal detail behind the part or to shorten a long continuous part.

  - Dimension Line		Shows distance.  Arrows drawn on the ends.

  - Extension Line		Shows where a dimension starts and stops.  Used with dimension lines, Line is 1/16” away from object.

  - Long Break Line		Shorten very long objects with uniform detail.  Typically represented as a jagged cut or break.

  - Leader Line	Show dimensions of arcs, circles and detail

- Short Answer

  - Put the following lines in order of precedence: Cutting Planes, Hidden Lines, Object Lines, Center Lines (Cutting plane, Object, Hidden, Center)

  - How do you pick the front view for a drawing?

    - Most natural position or use

    - Shows best shape and characteristic contours

    - Longest dimensions

    - Fewest hidden lines

    - Most stable and natural position

  - What is the difference between a Cavalier Oblique drawing and a Cabinet Oblique drawing?

    - Cabinet is half depth while Cavalier is full depth

- Sketching:  The following three pictures are of the same object where each cube is 0.5” x 0.5” x 0.5”.  Select the best front view for each image.

Orthogonal (Orthographic) Projection (Use four grids to represent the length of the side of a single cube)

Isometric Projection (Use one grid to represent the length of the side of a single cube)

Complete an Oblique Drawing of the following

One-Point Perspective

Two-point Perspective