## Slide 1: Getting Started in RobotC
// Comment
task
main()
motor[]
{}
wait1Msec()
;
=
Header
Code
Compile
Download
Run
Take out your notes.

## Slide 2: Learning Objectives
Understand the fundamentals of programming a robot.
  Programmer and Machine
  Planning and Behavior
  Basic RobotC Rules
Understand how to use the Motors and Sensors Setup to configure your robot.
Write a program for a Robot to complete some simple tasks.

## Slide 3: Fundamentals
Take notes (Ideas, commands, punctuation..)
Be prepared to share one thing you learned or was reinforced in the video.
Click on Fundamentals
Watch and take notes on these four short videos.

## Slide 4: Introduction to Programming
Search VEX Cortex Video Trainer or go to the following website.
http://education.rec.ri.cmu.edu/products/cortex_video_trainer/
  There is also a link on the class website.
Click on the ‘Fundamentals’ button
Watch and take notes on the videos for
  2. Planning and Behaviors
  3. RobotC Rules Part 1
  4. RobotC Rules Part 2
Be prepared to share one thing from each of the videos.
Take the quizzes that are after the videos to check for understanding.

## Slide 5: Getting Started in RobotC
Open RobotC
Select VEX 2.0 Cortex Platform
  Robot-> Platform ->VEX 2.0 Cortex
Make the robot compile to Virtual Worlds
  Robot-> Compiler Target -> Virtual Worlds
Select Virtual World
  Window->Select Virtual World to Use -> Curriculum Companion
Start a new file
  File – New File

## Slide 6: Your Robot

## Slide 7: Configuring the Robot: Focus on Motors
Robot -> Motors and Sensors Setup
Select the motor
  Currently can only purchase 393 Motors, also modify for internal gearing (high speed, turbo speed)
Naming Convention
  Rules
    Start with a letter
    No spaces, punctuation or reserved words (blue)
  Style
    Describes what it represents
    First letter is lowercase
    otherWordsStartWithUppercaseLetters
  For these motors
    leftMotor
    clawMotor
    armMotor
    rightMotor

## Slide 8: Motors and Sensors Setup Page
1) Select the ‘Motors’ tab.
6) Complete the setup for the remaining motors.
3) Use the pull down menus to select the motor.
4) The left motor will need to be reversed so the robot does not go in circles.
5) Select the side for drive motors.
7) Click on Apply to remember the changes.
2) Name the motor in the desired port.

## Slide 9: Motors and Sensors setup creates ‘pre-processor directives’

## Slide 10: Now we can start looking at RobotC
motor[motorName] = motorPower;
wait1Msec(milliseconds);

## Slide 11
The Header
// In front of the line makes this line a comment
/* */ for multiple line comments.
task main()
Marks the beginning of the instructions for the Robot.
RobotC Is CaSe SeNsItIvE!
motor[rightMotor] = 127;
motor[] Used to select the motor.
rightMotor = This represents the place where the motor is attached.
motor[port10] = 127; does the same thing.
= 127;
127 = full power
-127 = Reverse
0 = stop
wait1Msec(2000);
The robot continues what it was doing for (2000) milliseconds.
Two seconds in this case.
{}
Marks the begin and end of a block of code
Vocabulary
//
Comment
task
main()
motor[]
{}
wait1Msec()
;
=
Header
Code
Compile
Download
Run
; is used to mark the end of a command.
What do you think this code will do?
Code Break. Open RobotC, configure the motors and enter the above code.
Notes: Advanced students can also download the program to their physical robot.

## Slide 12: Testing the Program
Compile the program
  Changes into machine code that the robot understands.
Download the program
  Moving the machine language to your Virtual or Physical Robot
Virtual Robot
  Log in
  Select Robot
  Select Challenge
  Start Activity

## Slide 13: Compiling the Program

## Slide 14: Oops!
The compiler catches syntax (typing) errors and gives some hints on how to fix them.

## Slide 15: Errors
Errors and hints on the bottom of the page. If you click on an error it will highlight the line of the error.
Red X = error
Yellow X = Warning
Any guesses on how to fix these mistakes?

## Slide 16: Corrected and Compiled

## Slide 17: Download the program
Since we set it up to map to Virtual Worlds it will download to a Virtual Robot.

## Slide 18: Set up and Account with CS2N. It will track progress. Can log in locally as a guest without tracking.
Create an Account for you in CS2N

## Slide 20: Select Your Robot
1) Robots Tab
2) I will be using the Clawbot for discussion

## Slide 21: Select Activity: Utility-> Imperial Distance Utility
1) Utility Tab
2) Imperial Distance Utility
3) Start Activity

## Slide 22: Select Camera and Go
Follows Right
Scroll: Zoom
2) Top Down View
3) Free Movement:
Scroll: Zoom
Click-Drag: Rotate View
Show Sensors Toggle
Play: Run the program
Reset
Home

## Slide 23: Your Turn
Enter the Sample program
  Motors and Sensors Setup
  task main() and code
Compile and correct errors
Download to the virtual robot
Run the program
Reference Website:
http://education.rec.ri.cmu.edu/products/cortex_video_trainer/
Click on Movement for much of the material covered
Notes: http://education.rec.ri.cmu.edu/products/cortex_video_trainer/lesson/index_movement.html

## Slide 24: How the Challenges are Graded
Movement: Basketball Drills
Programming (10 Points = 100%)
___ Program compiles (4 points)
___ Header complete with names, description and date (2 points)
___ Code is properly indented (2 points)
___ Comments in the program describing the code (2 points)
Performance (10 points = 100%)
____ Completed

## Slide 25: Assignment
Complete the following Challenges
Basketball Drills
Sentry Simulation I
Labyrinth Challenge.
For each Challenge, demonstrate the solution to Mr. Smith and have your code graded.
Save your Solutions in the Movement Challenges Folder.