## Slide 1: VEX Structure
The VEX structural pieces all contain square holes (0.182” sq) on a standardized 0.5” grid.
The smaller diamond holes are there to help users cut pieces using tin snips or fine toothed hacksaws without leaving sharp corners.
Steel and Aluminum

## Slide 2: Screws
8-32 screws for attaching structure
  Use 3/32” Hex Key
  ¼” to 2” Lengths
  Locking Screws: Like normal screws but harder to remove (First 10-12 times)
  Shoulder Screws (0.20” Long Shoulder)
  ½” Plastic Thumb Screws
6-32 Screws for Motors and Servos
  Use 5/64” Hex Key
  ¼” and ½”
  ½” Locking

## Slide 3: Screws
8-32 x 0.125” Setscrew for Shaft Collars
Couplers: 0.500” and 1.000”
  Used for connecting Standoffs

## Slide 4: Nuts
8-32 Thread
Keps
Nylock
Hex

## Slide 5: Bars, ‘C’-Channels, Angles, Rails
Bars (1x25)
  Can be bent, but will never again be straight
C-Channel
  1x2x1x35, 1x3x1x35, 1x5x1x25, 1x5x1x35
  Added strength and twist resistance
Angles
  2x2x25, 2x2x35, 3x3x35
  Used for framing, good strength in two axis
Chassis Rails
  2x1x25, 2x1x35
  Tab at the end allows more connection options.
Notes:   http://curriculum.vexrobotics.com/curriculum/intro-to-robotics/vex-robotics-design-system

## Slide 6: Structure: Plates and Base Plates
Base Plate
  15 x 30
  Create a large stationary robotic arm, or interlock them to build larger manufacturing type systems.
Plates
  15x5 , 25 x 5

## Slide 7: Structure: Gussets
45 Degree
90 Degree
Gusset Pack:
  Pivot Gusset: Connect parts and angles 0 – 90 Degrees
  Plus Gusset: Strengthen flat joints
  Angle Gusset: Strengthen ‘T’ Joints
C-Channel Coupler: Connect two 1x2x1 ‘C’ Channels
Angle Coupler: Connect two 2x2 Angles
Angle Corner

## Slide 8: Structure: Standoffs (8-32)
0.25” – 6.00”
Tapped on both ends to fit 8-32 Screws
Add spacing

## Slide 9: Structure: Other
Latex Tubing: Elastic
Rubber Bands (#32 or #64)
Zip Ties (4” and 11”)
Anti-Slip Math (Thin, Thick)